## Slide 1
Les Talelas
IEEE AESS Sustainabilty
Hackathon
Theme 4 : Sustainable Space Systems & Orbital Lifecycle
Because the sky shouldn't wait
for someone on the ground to fix it.

## Slide 2
Les Talelas
IEEE AESS Sustainabilty
Hackathon
Theme 4 : Sustainable Space Systems & Orbital Lifecycle
Because the sky shouldn't wait
for someone on the ground to fix it.

## Slide 3
IEEE AESS Sustainabilty
Hackathon
Problem Statement
Low Earth orbit is under severe pressure.
There are more than 1,2 million debris objects!

## Slide 4
IEEE AESS Sustainabilty
Hackathon
Problem Statement
Low Earth orbit is under severe pressure.
There are more than 1,2 million debris objects!
More than 40% of small satellites launched between 2000 and 2016 experienced failure.

## Slide 5
IEEE AESS Sustainabilty
Hackathon
Problem Statement
Low Earth orbit is under severe pressure.
There are more than 1,2 million debris objects!
More than 40% of small satellites launched between 2000 and 2016 experienced failure.
Sensor Degradation
Faulty Data
Loss of Trust
Early Decommission

## Slide 6
IEEE AESS Sustainabilty
Hackathon
Proposed Solution

## Slide 7
IEEE AESS Sustainabilty
Hackathon
Proposed Solution
We don’t need more hardware in space. We need smarter software.

## Slide 8
IEEE AESS Sustainabilty
Hackathon
Proposed Solution
NUWA, the first complete, autonomous, self-healing ecosystem for satellite constellations.
NUWA transforms a group of fragile, isolated spacecraft info a cooperative, resilient network.
Keep satellites useful for longer, so we replace fewer of them
We don’t need more hardware in space. We need smarter software.

## Slide 9
The Ecosystem & Core Services

## Slide 10
IEEE AESS Sustainabilty
Hackathon
The Ecosystem & Core Services
Correction
1
Relay
2
Borrow
3
Deterministic C++ state machine with 21 states & 24 events

## Slide 11
IEEE AESS Sustainabilty
Hackathon
The Ecosystem & Core Services
Correction
Deterministic C++ state machine with 21 states & 24 events
DEGR wheighting & median-Kalman filter
Relay
2
Borrow
3
1

## Slide 12
IEEE AESS Sustainabilty
Hackathon
The Ecosystem & Core Services
Relay
2
Borrow
3
Correction
1
Route vital data through neighbours
Deterministic C++ state machine with 21 states & 24 events

## Slide 13
IEEE AESS Sustainabilty
Hackathon
The Ecosystem & Core Services
Borrow
3
Correction
1
Relay
2
Failed sensors are bypassed by streaming a neighbors' healthy data
Deterministic C++ state machine with 21 states & 24 events

## Slide 14
IEEE AESS Sustainabilty
Hackathon
The Ecosystem & Core Services
Correction
1
Relay
2
Borrow
3
Deterministic C++ state machine with 21 states & 24 events
-Validation on the European Space Agency’s OPSSAT-AD dataset
-SVD Anomaly Detector Pipeline
Preventing
27,8
Replacement Satellites
Or future debris-risk
Saving
8,3m
Tons of CO² equivalent
launch emissions
Reduces unnecessary
mass sent to orbit
-Achieving 0,99 accuracy : Under a 437 MHz UHF link model
-Maintains 9dB of link margin at around 1000 km.
-Estimated usable range of 2800 km.

## Slide 15
IEEE AESS Sustainabilty
Hackathon
Impact
Preventing
Across a 50-year reference industry growth-model
27,8
Replacement Satellites
Or future debris-risk
Saving
8,3m
Tons of CO² equivalent
launch emissions
Reduces unnecessary
mass sent to orbit

## Slide 16
IEEE AESS Sustainabilty
Hackathon
SDG Alignment

## Slide 17
IEEE AESS Sustainabilty
Hackathon
Scalability
Shared computation
Faster fault detection
Multi-band communication
Encryption layer

## Slide 18
IEEE AESS Sustainabilty
Hackathon
We are already within the process of forming a scientific paper for SISP

## Slide 19
IEEE AESS Sustainabilty
Hackathon
Conclusion
->We don’t need to launch more backup hardware into space. Like the myth, our project NUWA patches the collapsing orbital architecture from within, replacing physical debris risks with intelligent, cooperative software.

## Slide 20
IEEE AESS Sustainabilty
Hackathon
Meet Our Team
Rayen Khammar
Adem Bhouri
Akrem Medimagh
Iyed Mdimegh
Talel Laarif

## Slide 21
IEEE AESS Sustainabilty
Hackathon
Thank you
for your attention !

## Slide 22
IEEE AESS Sustainabilty
Hackathon
The Empirical Validation
Protocol Boundedness
273/273 assertions passed
Correction Integrity
94,3% RMSE improvement
Relay Resilience
100% payload reconstruction

## Slide 23
IEEE AESS Sustainabilty
Hackathon
Mathematical Calculations
1-DEGR Trust Score & Correction Weight :
2-SVD Anomaly Detection :
4-DEGR-Wheited Kalman Correction :
5-Link Budget :
3-Mission Life Extension :
6-Packet Error Rate and Frame Energy :

## Slide 24
Refrences
Pitch fact / claim | Resource or calculation | Credibility
Low Earth orbit is crowded: over 1.2 million debris objects larger than 1 cm and over 50,000 larger than 10 cm. | ESA Space Environment Report 2025 states those debris population estimates. Source: ESA. | External, official agency source.
Small satellites are fragile: 41.3% of small satellites launched from 2000 to 2016 had total or partial mission failure. | NASA/NTRS technical report "Small-Satellite Mission Failure Rates". Source: NASA NTRS PDF. | External, NASA technical report.
Ground contact is limited; single-ground-station LEO access can be only a few contacts per day lasting minutes. | NASA report: fixed ground station can give 2-4 meaningful contacts/day with up to 5 minutes/contact. Source: NASA NTRS PDF. | External, NASA technical report.
NUWA uses real satellite telemetry for anomaly-detection validation. | OPSSAT-AD is an AI-ready anomaly-detection benchmark from ESA OPS-SAT telemetry. Source: Nature Scientific Data. | External, peer-reviewed dataset paper.
NUWA detects anomalies on-board using SVD-style telemetry modeling. | External basis: OPSSAT-AD benchmark validates satellite-telemetry anomaly detection. NUWA implementation: Hankel-SVD detector in HankelSVDDetector.js. | Mixed: peer-reviewed dataset plus project implementation.
SISP is a deterministic protocol layer with correction, relay, and borrow services. | State machine and protocol implementation in sisp_state_machine.cpp and sisp_protocol.cpp. | Project-specific, reproducible from source.
SISP uses a 21-state / 24-event C++ state machine and fixed 64-byte frames. | Design documented in SISP_RESEARCH_PAPER.md; code backed by state-machine and frame tests. | Project-specific, test-backed.
Protocol boundedness claim: 273/273 C++ assertions pass. | Test suite source in c++ implemnetation/tests; runner: run_cpp_tests.ps1. | Project-specific, reproducible test evidence.
Correction KPI: 94.3% RMSE improvement under 30-day drift. | Calculation: (8.909 - 0.504) / 8.909 = 94.3%; documented in SISP_RESEARCH_PAPER.md. | Project-specific, simulation/test result.
Packet-loss KPI: 85.6% RMSE improvement under 10% packet loss. | Calculation: (8.290 - 1.197) / 8.290 = 85.6%; documented in SISP_RESEARCH_PAPER.md. | Project-specific, simulation/test result.
Relay resilience: 109/109 bytes reconstructed through corruption, reordering, retry, and replay disruption. | Relay test source: test_relay_text_resilience.py. | Project-specific, reproducible integration test.
Energy overhead: 8-neighbor correction takes about 1.10 s and 3.66 J; daily overhead is about 317 mWh. | Calculation: (10 W + 8*2.5 W)*0.122 s = 3.66 J; daily model documented in SISP_KPI_SNAPSHOT.md. | Project-specific engineering model.
Link assumption: 437 MHz UHF dual profile with 9,600 bps control and 19,200 bps bulk. | Link-budget study and formulas in SISP_RESEARCH_PAPER.md. Hardware realism cross-check: official SDR list prices from Ettus B210 and Ettus N310. | Project model plus real hardware market check.
Launch replacement cost floor starts at public rideshare pricing. | SpaceX official rideshare pricing: $350K for 50 kg to SSO plus $7K/kg additional mass. Source: SpaceX Rideshare. | External, official commercial pricing.
Ground-station operations can be treated as pay-per-use in cost models. | AWS Ground Station uses on-demand and reserved antenna access, paid by antenna time used. Source: AWS Pricing and AWS FAQ. | External, official commercial pricing model.
Sustainability impact: fewer premature replacements reduce launch emissions, mass to orbit, and future debris pressure. | Transparent scenario model: baseline 100 / 3 = 33.33 replacements/yr; improved 100 / 4.35 = 22.99 replacements/yr; avoided 10.34/yr. CO2 and mass results scale from avoided replacements. | Model estimate, not flight measurement.
Rocket launches have climate and atmospheric impact. | Review source: Dallas et al., "The environmental impact of emissions from space launches"; broader NASA atmospheric impact review also supports concern. Sources: ADS abstract, NASA TM. | External scientific literature.
NUWA is not yet flight-qualified. | Project limitation in evidence sheet and research paper: current validation is simulation, unit/integration tests, and hardware-in-loop roadmap. | Honest limitation; needs flight/hardware validation.

## Slide 25
CREDIBLE VALIDATION
$250K-$700K
software, simulation, COTS-radio lab
FLIGHT-DEMO READINESS
$900K-$2.5M
partner testbed, security, mission docs
OPTIONAL HOSTED DEMO
$150K-$750K+
depends on mission partner access
Cost area | What we buy | Lean | Strong validation
Core engineering | C++ flight stack, SVD detector, simulation, CI | $80K-$180K | $250K-$600K
RF / HIL lab | COTS UHF radios, SDRs, attenuators, power tools | $20K-$70K | $100K-$300K
Mission testing | flatsat work, partner telemetry, operator review | $30K-$100K | $150K-$500K
Security + reliability | auth frames, replay defense, FMEA, QA hardening | $10K-$40K | $50K-$150K
Cloud + tooling | dashboards, scenario runners, data storage | $5K-$20K | $25K-$80K
Legal / compliance | IP, contracts, export-control review | $10K-$50K | $50K-$150K
IEEE AESS Sustainabilty
Hackathon
Cost Structure

## Slide 26
IEEE AESS Sustainabilty
Hackathon
Deployment Cost / Partner
Commercial target
$150K-$400K
our first-year delivery cost per normal operator
Ongoing support
$50K-$150K/yr
updates, validation, dashboards, mission support
Value floor
$350K+
public SSO rideshare slot before satellite build cost
Buyer type | Typical scope | Our first-year cost | Our annual cost
Research / university | 1-5 satellites; simulation-first | $8K-$30K | $3K-$12K
Small operator | 5-20 satellites; pre-flight integration | $50K-$160K | $20K-$70K
Commercial constellation | 20-100+ satellites; mission adapters | $180K-$600K | $60K-$220K
Agency / high-assurance | security review, audit, formal validation | $500K-$1.5M+ | $150K-$500K
Recommended offer
Setup/integration: $250K-$1M depending on assurance level
Recurring license: $2K-$10K per satellite per year
100-satellite buyer: $500K-$900K first year; $300K-$700K/year after